## Slide 1: Computer Architecture Tutorial 2
2015 / 4 / 7
First Submission: 2015 / 5/ 9
Second Submission: 2015 /5 / 16

## Slide 2: Outline
Project 1 – Issues
  Testing Script & Golden Simulator
Project 2 - Pipeline
  Concept
  Output & Input
  Implementation Notes
Notes: Why?

## Slide 3: Download the New Appendix-B from Project 2 on iLMS

## Slide 4: Project 1 - Issues
Sll $0 $0 C, if C != 0 then write error Else NOP
Valid testcase can not lead to number overflow by beq, bne.
beq , bne , slt use C operation ( >,<,=…etc)

## Slide 5: Testing Script & Tool

## Slide 6: Run Golden Simulator
Type /home/archi/single_cycle
Refer to the .rpt file

## Slide 7: Test your folder structure
Execute the “test_script.py”
  Type python test_script.py
  Enter your student ID
  Enter the project number
You should check whether you get 9 “OK” conditions

## Slide 8: Project 2 - Pipeline
Improve instruction-level parallelism(ILP)

## Slide 9: Single Cycle Data Path
Low design complexity,
Low ILP ( instruction-level parallelism ), How to improve?
Notes: 為什麼要介紹 Data Path ?
Revisit single cycle的simulator，但是在上次的課程中，我們加入Data Path的觀念，
反應硬體實際實作，幫助導入pipeline的結構。
為什麼 Design Complexity 比較低呢？在一次 clock 就完成完整一個指令 ( instruction) 的工作。

## Slide 10: Pipeline Stage
DM
EX
EX/DM
DM/WB

## Slide 11: Pipeline Datapath & Control ( Project 2 Objective)
Higher design complexity
High ILP(instruction-level parallelism)
Notes: 1, 為達到增加instruction-level parallelism，

## Slide 12: Pipeline 5 Stages
IF
  instruction fetch
  PC+4
ID
  Read Register File
  Sign extension
  Control unit decode
  Hazard detect, Branch/Jump detect
EX
  ALU / Branch
DM
  Access data memory
WB
  Write value to Register File
independent of instruction type
dependent of instruction type R-type, I-type, J-type
Forwarding Unit
EX/DM to ID
EX/DM to EX
DM/WB to EX

## Slide 13: Project 2 Objective Solving Pipeline Hazard
Data hazard
  Stall , Ex: lw is not write back yet.
  Forwarding ( appendix C-2 )
    EX/DM to ID
    EX/DM to EX
    DM/WB to EX
Control hazard
  Flush (appendix C-2 ex5 )

## Slide 14: Input & Output
Input: same as project 1
Output:
  snapshot.rpt
    Contents of registers
    Mnemonic in pipeline stage
      whether stalled in next cycle
      whether forwarding in this cycle
  error_dump.rpt
    Appendix D ( Be careful about error order )

## Slide 15: snapshot trace
lw $2, 0($3)
or $3, $1, $4
beq $2, $3, some_line
and $1, $1, $0
Execute cycle 4
detect right after
Cycle 3 is done!
Detect stalled
Forwarding
EX/DM

## Slide 16: Test Case Design
Your test case need to include:
  One control hazard
  One data hazard resolved by inserting NOPs
  One data hazard cleared by forwarding
Number of NOPs and forwarding path is unlimited.
< 500,000 cycles
(Valid rule is same as Project 1)

## Slide 17: Implementation Notes
NOP: sll $0, $0, 0 (bit-stream 0x00000000 recomm.)
Initialization: The pipeline is initialized with NOPs in all stages
Terminates: after five “halt”, otherwise invalid
Simulation Order (highly recommended)
  WB  DM  EX  ID  IF
  To avoid re-execution of some stages

## Slide 18: Submission
Upload to iLMS
Name executable file pipeline
File name format : (more detail in spec)
  Program: studentID_02.tar.gz
  Report: studentID_report.pdf
Check your Program Package pass the testing script
Or check your can untar /make …etc by yourself

## Slide 19: Submission (2)
Create a folder named studentID_02 under /home/archi/studentID
In the folder, please provide the following two folders and corresponding files required:
  simulator : contains your「Makefile」,「README」, and 「source code files」.
    Your Makefile should support the following two functions: make – to build your simulation environment make clean – to erase from the build tree the files built by make all.
  testcase : contains your test case files.

## Slide 20: Submission (3)
  Finally, compress the folder studentID_02 as studentID_02.tar.gz
Compress
  tar -zcvf 學號_02.tar.gz 學號_02
Decompress (TA will use this )
  tar -zxvf 學號_02.tar.gz
StudentID_02
(folder)
testcase
(folder)
simulator
(folder)

## Slide 21: tar 指令

## Slide 22: tar 指令
壓縮： tar -zcvf 學號_01.tar.gz 學號_01
解壓縮： tar -zxvf 學號_01.tar.gz
  -c ：建立一個壓縮文件的參數指令
  -x ：解開一個壓縮文件的參數指令
  -z ：是否同時具有 gzip 的屬性
  -v ：壓縮的過程中顯示文件
  -f ：使用檔名，在 f 之後要立即接檔名

## Slide 23: Evaluation
Report: (Same as project 1)
Test Case: (Same as project 1)
Simulator :TA will use linux diff to compare snapshot.rpt and error_dump.rpt for grading

## Slide 24: Test Environment
ssh studentId@140.114.75.140
Data Transmission: FileZilla , scp, ftps
Any related issue and problem
  Please post your issue / problem on iLMS

## Slide 25: snapshot.rpt format
Pipeline Stage
Contents of registers